| O.O. | 16-02771-OO | MISO No. | 1-11304250 | File No. | 240802 |
| --- | --- | --- | --- | --- | --- |
| Name of Outage: | 115 kV Line I1F (Border – Island Falls) |
| Effective Dates: | 2016-09-27 from 0800 to 2016-09-28 at 1600 CDT (2016-09-27 from 0800 to 2016-09-28 at 1600 EST) |
| Standing Guide Reference: | MH-SPCN Standing Guide |

| Description of Work: | Insulation Tests on Border I1F Line CVT's and I1F Sync Pot, communications wavetraps, teleprotection & PLC maintenance, cut risers clear at Mile 13 on 115 kV Switch 1013 switch for a Permanent open point since salvage of Mile 13 Station. |
| --- | --- |
|  | TRANSFER Limits: MH-SPCN West (MH Export) SOL: 25 Schedule Limit 15 Location TTC RM Transfer OM Schedule Limit (SOL) Firm Non-Firm West 25 0 25 10 15 0 15 MH-SPCN East (MH Import) SOL: 70 Schedule Limit 60 Location TTC RM Transfer OM Schedule Limit (SOL) Firm Non-Firm East 70 0 70 70 0 60 60 |

| MISO RC INFO | System Intact FIRM SCHED LIMIT DYNAMIC SCHED LIMIT SOL TLR1 TLR3 MH-SPC_West (MH Export) 15 15 25 23 24 MH-SPC_East (MH Import) 0 60 70 65 67 |
| --- | --- |
|  | MISO Webtool Manual Override is Required MISO Webtool Postings TTC Firm TRM Non-Firm TRM Coeff MH_SPC _West (Export) 25 10 10 1.000 MH_SPC_East (Import) 70 70 70 0.143 |
| Special Instructions: | TOI Extensions - This TOI may be extended until 23:59 by performing the following steps: Verify system conditions to confirm there are no additional tie line facilities outages, or new internal MH outages. Review RTCA to confirm there are no new contingencies. Contact MISO to confirm there are no new outages, if there are no new outages provide notice to MISO that MH is extending the TOI. Extend the outage in COLA. Update TLAP outage table. Provide notice to affected balancing authorities |

| Prepared By: | D. Williams | Date: | 2016.09.14 |
| --- | --- | --- | --- |
| Revised By: | S.W.Saboraki | Date: | 2016.09.16 |

Copies to:

SOSS, System Control Centre		NSSS, System Control Centre

GSSS, System Control Centre		GSO, System Control Centre

Operating Order		File 240802

MHEB OASIS		MISO – St. Paul

SPC – Yong Zheng		SPC - Colin Nicholson