2016 RFP

Attachment 20: PacifiCorp High Level Cost Estimates Associated With Integration

Draft (9-22-2011)

Preliminary Assessment of Transmission Impacts Associated with

RFP Points of Delivery

- Overview of Points of Delivery

PacifiCorp is interested in resources that are capable of delivery into or in a portion of the Company’s network transmission system in the eastern balancing area.  Specifically, the point(s) of delivery of primary interest to PacifiCorp are:

East system Points of Delivery

- Salt Lake Valley

  - Connected to a major 138 kV or 345 kV substation in the Wasatch Front load area south of the Ben Lomond substation and north of the Camp Williams substation.

- PacifiCorp Sites

  - Currant Creek

- Mona 345 kV

- Glen Canyon 230 kV

- Nevada/Utah Border:

  - Gonder-Pavant 230 kV line known as “Gonder 230 kV”

  - Red Butte – Harry Allen 345 line known as “NUB” or Red Butte 345 kV

- Crystal 500 kV

- West of Naughton

  - Connected to a major 230 kV or 345 kV substation west of Naughton substation to the Utah border.

Although the Company will consider resources delivered to the following areas these areas have been identified as having potential transmission constraint implications and as such, will need to be evaluated accordingly:

- Wyoming, unless the resource(s) electrically reside south of the Naughton Monument 230kV line. If, resources in Wyoming are not electrically west of Naughton such resources may be useful in supporting the increased load and wind resources in Wyoming; however, such resources may be negatively affected by transmission constraints.

- All points of receipt which require transmission line construction will require 4-7 years and in some scenarios even longer in order to allow time for environmental work, route selection, permitting, and construction.  Resources located at one of these POR’s may require cost adjustment for some period of time to accommodate re-dispatch of existing resources or other means of managing transmission congestion in the interim period between completion of plant construction and before new transmission is commissioned.

- Estimates provided in the document are conceptual (plus or minus 50%) un-scoped and provided for informational purposes.  System impact studies completed for actual generation interconnection request may identify new constraints and impacts that significantly change the cost and schedule estimates provided here.  Cost estimates and schedules provided in this document do not represent any firm offer of service.

PacifiCorp is willing to consider purchasing capacity and associated energy that is sourced from Desert Southwest (Nevada, California, Arizona, New Mexico); provided, the selling entity is able to purchase firm transmission from the resource to either Gonder or Nevada Utah Border.

West System Points of Delivery include

- Mid Columbia – Yakima Area

  - Midway 230 kV

  - Wanapum 230 kV

- California Oregon Border

- Portland

  - Troutdale 230 kV

- Willamette Valley

  - Alvey 500 kV

  - Fry 230 kV

- Southern Oregon

  - Chiloquin230 kV

  - Dixonville 230 kV

  - Meridian 230 kV

  - Reston 230 kV

- Central Oregon

  - Bend 69 kV

  - Pilot Butte 69/230 kV

  - Ponderosa 230 kV

  - Redmond 69 kV

- Oregon Coast

  - Astoria to Tillamook 115 kV

  - Boyer (Lincoln City) 115 kV

- Within the Western Control Area – The point of interconnection is the point between the resource, or the electrical system to which the resource is connected, and PacifiCorp’s transmission system.

- Scheduled to the point(s) of interconnection between PacifiCorp’s western control area and the Bonneville Power Administration or Portland General Electric such that transfer limitations are not exceeded.  If the resource is located within the Bonneville control area the Bidder must show they have control area service from the resource to the delivery point.

- All points of receipt that require transmission line construction will require 4-7 years and in some scenarios even longer in order to allow time for environmental work, route selection, permitting, and construction.  Resources located at one of these POR’s may require cost adjustment for some period of time to accommodate re-dispatch (if possible) of existing resources or other means of managing transmission congestion in the interim period between completion of plant construction and before new transmission is commissioned.

- Transmission Assumptions Associated with the Points of Delivery

PacifiCorp may need to increase transmission import capability and upgrade its network system capacity in order to integrate a resource delivered to the preferred points of delivery. The table below indicates the possible additions necessary and the indicative cost associated with the upgrade.  These indicative costs are based on assessments done by the PacifiCorp Transmission group for current and past Integrated Resource Plan and System Impact Studies.

These cost estimates are indicative but will be used for the purpose of evaluating bids and may be refined if better estimates are received prior to issuance of the RFP.

| East System |  |  |  |  |
| --- | --- | --- | --- | --- |
| Point of Delivery | Description of Possible Transmission Additions / Upgrades | Path(s) to Upgrade and Voltage Support | Estimated Cost of Upgrades | Transmission In Service (estimate) |
| Salt Lake Valley 138 kV 600 MW | Upgrades to existing lines | Unknown location | $108M | 2016 |
| Mona/ Currant Creek 345 kV 600 MW | Substation upgrades | Mona to PACE | $67M | 2013 |
| Glen Canyon 345 kV 600 MW | Transmission line(s), substation, phase shifter | Glen Canyon to Sigurd and Mona to PACE | $382M | 2019 |
| Gonder 345 kV 600 MW | Transmission line(s), substation | Gonder/Nev Border to Sigurd and Mona to PACE | $336M | 2018 |
| NUB (Harry Allen 345 kV) 449 MW Summer, 524 MW Winter | Series Compensation on Sigurd to Mona transmission lines. Requires wheeling across the NV Energy transmission system to the PacifiCorp system + Sigurd to Red Butte #2 line. | Sigurd/Huntington north | $76 M | Mid 2015 |
| Crystal 500 kV 600 MW | Transmission line(s), substation, transformer, phase shifter | Crystal to RButte + RButte + Clover to PACE | $549 M | 2020 |
| Wyoming 400 MW | Transmission line, substation + planned Energy Gateway capacity | Dave Johnston to Windstar line, Dave Johnston and Windstar substation additions | $173 M | 2018 |
| Populus 345 kV, 600 MW | Substation connection. Delivery requires use of existing firm network allocation rights across Path C. | N/A | $30 M | 2014 |
| Four Corners 345kV 600 MW | New line, terminations, phase shifter | F.Corners to Clover + Clover to PACE | $798M | 2019 |

| West System |  |  |  |  |
| --- | --- | --- | --- | --- |
| Point of Delivery | Description of Possible Transmission Additions / Upgrades | Path(s) to Upgrade and Voltage Support | Estimated Cost of Upgrades | Transmission In Service (estimate) |
| Mid Columbia Paul 600 MW | Delivered load to Yakima POD – of Wanapum and Vantage | N/A | No Cost | 2013 |
| California Oregon Border 600 MW | Delivered to southern Oregon load via Malin 230 kV – 200 MW delivered to Southern Oregon and up to 400 MW delivered to the Willamette Valley through a new or double circuit 230 upgrade through Alvey. | 230 kV line Alvey to Dixonville substations, additions at Alvey and Dixonville | $314 M | 2018 |
| Portland Troutdale 400 MW | Transmission line, substation additions | 230 kV line Gresham to Bethel substations, additions at Gresham and Bethel | $216 M | 2018 |
| Willamette Valley – Alvey 230 KV 400 MW | Transmission line, substation additions | 230 kV line Alvey to Dixonville substations, additions at Alvey and Dixonville | $314 M | 2018 |
| Chiloquin Southern Oregon 400 MW | Transmission line, substation additions | 230 kV line Chiloquin to Klamath substations, additions at Chiloquin and Klamath | $108 M | 2017 |
| Southern Oregon 588 MW | Integrate existing interconnected, third party, generation. | N/A | N/A | N/A |
| Southern Oregon 600 MW | Substation, | New 500/230 kilovolt substation between Meridian and Grants Pass or Klamath Falls substations | $55M | 2015 |

# Footnotes

The costs are shown in current year (2011) up-front capital dollars.

Date reflects Dec 31 of  the stated in service date unless otherwise stated. .

Requires completion of the Mona to Oquirrh transmission line which is currently under construction.

Sigurd to Red Butte #2 is  required for load service to SW Utah and excluded from costs for this resource.

Installation of series compensation to support NUB imports completed three years after notification of need.

Assumes the proposed 230 kV Vantage to Wannapum line, required for load service to Yakima is constructed as planned